## Slide 1
MegaNet MVP
Internet Paralela Descentralizada
Kim Dotcom's Vision | Python Prototype | 2026-02-23
Hacking Conference 2026 | Security Research Track

## Slide 2
The Problem: Internet is Centralised & Censored
The centralised internet has critical weaknesses:
IP addresses are assigned by IANA/RIRs -> can be revoked or blocked
DNS is centralised -> single point of control and failure
BGP routing is trust-based -> route hijacking, censorship
Traffic is monitorable at ISP level
Kim Dotcom's MegaNet vision:
No IP addresses -> addresses derived from public keys
No DNS -> blockchain-based key registry
Radio transport (LoRa) -> censorship-resistant physical layer
Encrypted by default -> E2E, no plaintext on the wire

## Slide 3
Architecture: 5 Independent Layers
Layer 1 CRYPTO Ed25519 identity + X25519 ECDH + ChaCha20-Poly1305
Layer 2 BLOCKCHAIN SHA3-256 PoW | 4 TX types | fork resolution
Layer 3 LORA RADIO EU868 propagation model | duty-cycle tracker
Layer 4 KADEMLIA DHT 160-bit XOR routing | k=20 | content-addressing
Layer 5 NODE Integration: send_message / receive_packets / mine_block
Single external dependency: cryptography>=42.0.0
42 unit tests | 0.16s runtime | no hardware required
Each layer is independently testable and replaceable.
Real LoRa hardware can replace the simulator with zero changes to upper layers.

## Slide 4
Cryptography: Public-Key Addressing & E2E Encryption
# Node identity & address
ed_priv, ed_pub = Ed25519.generate() # signing / identity
x_priv, x_pub = X25519.generate() # ECDH key exchange
address = SHA3_256(ed_pub_raw)[:20] # 160-bit, no registry needed
# Message encryption A -> B
shared = X25519(A.x_priv, B.x_pub) # 32-byte secret
aad = A.addr + B.addr # authenticated metadata
nonce = os.urandom(12) # 96-bit random
ct = ChaCha20Poly1305.encrypt(shared, plaintext, aad, nonce)
wire = A.addr(20B) + nonce(12B) + ct
ChaCha20-Poly1305: constant-time, hardware-independent, 256-bit security
Perfect for IoT/LoRa: no AES hardware required | lower power consumption

## Slide 5
Lightweight Blockchain: Registration, Routing & Receipts
# 4 Transaction types (all Ed25519 signed, SHA3-256 tx_id)
NODE_REGISTER -> publish ed25519_pub + x25519_pub
ROUTING_UPDATE -> announce up to 10 known peers
MESSAGE_RECEIPT -> non-repudiable delivery proof (msg_id + receiver)
DATA_ANCHOR -> pin content_hash + frag_count on-chain
# Proof of Work (demo settings)
difficulty = 2 # 2 leading hex zeros = ~256 iterations = ~1ms/block
hash = SHA3_256(JSON(block_header)) must start with '00'
# Mempool: max 50 txs, FIFO eviction, dedup by tx_id
# Fork resolution: longest valid chain wins
State indices rebuilt from chain: node_registry, message_receipts, data_anchors

## Slide 6
LoRaWAN EU868: Radio Transport Without IP
# Log-distance path loss model
PL(d) = 112 dB + 10 * 2.7 * log10(d_km) # n=2.7 rural/suburban
RSSI = 14 dBm - PL(d) # TX power 14 dBm (EU868 max)
# Delivery probability (sigmoid)
P(rx) = 1 / (1 + exp(-0.5 * (RSSI - sensitivity[SF])))
# EU868 Duty cycle: 1% per hour (sliding window)
budget = 36,000 ms / hour # enforced per gateway
RSSI @ 1km: -98 dBm @ 5km: -117 dBm @ 10km: -125 dBm @ 15km: -130 dBm
SF7 sensitivity: -123 dBm -> effective range ~7-9 km
5 gateways on 20x20 km grid | Fragment size: 203 B (SF7: 222B - 19B header)
Real LoRa hardware plug-in: replace LoRaSimulator.transmit() with SX1276 driver

## Slide 7
Kademlia DHT & 'Homeless Data'
# 160-bit XOR routing (matches 20-byte address space)
bucket_idx = (our_addr XOR their_addr).bit_length() - 1 # 0..159
k = 20 # contacts per bucket, LRS eviction
# Content addressing (homeless data)
content_hash = SHA3_256(data)[:20] # 20-byte content address
store_key = SHA3_256(content_hash + frag_idx)[:20]
# Fragmentation
fragment_message(data, max=203B) -> (content_hash, [Fragment...])
reassemble_message(fragments) -> bytes | None # None if incomplete
Data has no fixed home -> resistant to node takedowns
Any node holding fragments can forward/serve them
Content hash verified on reassembly -> data integrity guaranteed

## Slide 8
End-to-End Message Flow: Alice -> Bob
1. Lookup Bob.x25519_pub in blockchain.node_registry
2. shared_secret = X25519(Alice.x_priv, Bob.x_pub)
3. wire = Alice.addr(20B) + nonce(12B) + ChaCha20Poly1305(plaintext)
4. fragment_message(wire) -> chunks of <=203 bytes
5. for chunk in chunks:
pkt = LoRaPacket(SF7, chunk)
LoRaSimulator.transmit(pkt, Alice.x, Alice.y) # path loss + random
6. Gateways receive -> deduplicate -> deliver to Bob
7. Bob.receive_packets() -> reassemble -> decrypt -> Bob.inbox
8. Bob creates MESSAGE_RECEIPT tx -> mine_block() -> broadcast
9. On-chain proof: blockchain.message_receipts[msg_id]
Partitioned nodes cannot receive | All state verifiable on-chain

## Slide 9
Security Properties & Threat Model
Threats Addressed:
Eavesdropping -> ChaCha20-Poly1305 E2E encryption
Impersonation -> Ed25519 signatures on all transactions
Replay attacks -> Random 96-bit nonce per message
Payload tampering -> Poly1305 16-byte authentication tag
IP-based censorship -> No IP addresses in the protocol
Sybil (partial) -> PoW registration cost
MVP Limitations (known):
No key revocation | PoW difficulty=2 trivial (demo only)
No incentive model for relaying | No store-and-forward for offline nodes

## Slide 10
Test Results: 42/42 Tests Pass
$ .venv/bin/pytest tests/ -v
test_blockchain.py::test_genesis_deterministic PASSED
test_blockchain.py::test_fork_resolution_longer_chain_wins PASSED
test_blockchain.py::test_mempool_fifo_eviction PASSED
test_crypto.py::test_ecdh_symmetric PASSED
test_crypto.py::test_tamper_detection_raises PASSED
test_lora.py::test_rssi_at_5km PASSED
test_lora.py::test_duty_cycle_blocks_over_budget PASSED
test_lora.py::test_simulator_far_node_low_delivery PASSED
...
42 passed in 0.16s
No hardware | No network | Single dependency: cryptography>=42
python3 -m venv .venv && .venv/bin/pip install -r requirements.txt

## Slide 11
Live Demo: python main.py
$ python main.py
1. Node Creation
Alice: 4ae58a4f3022fe697a88d19edfa5b18350f1498c
Bob: 67005aedfde22015fe044a1811f0300638b9097f
[PASS] All addresses are 40 hex chars & unique
2. Bootstrap -> [PASS] node_registry has 5 entries | height >= 1
3. Alice->Bob -> [PASS] Bob received correct plaintext
4. Receipt -> [PASS] Chain grew to >= 2 | message_receipts populated
5. Partition -> [PASS] Partitioned node (Eve) received nothing
6. Routing -> [PASS] Alice has >= 4 contacts
7. DHT -> [PASS] 500B -> 3 fragments, reassembly correct
8. LoRa -> [PASS] RSSI @ 5km = -116.9 dBm (expected ~-117 dBm)

## Slide 12
Roadmap: From MVP to Production
Phase 1 (MVP - DONE): Pure Python simulation | 42 passing tests | full E2E demo
Phase 2 - Real Hardware:
Swap LoRaSimulator -> SX1276/SX1278 driver | Raspberry Pi / ESP32 nodes
Phase 3 - Protocol Hardening:
Key revocation | PoW difficulty 6+ | Difficulty adjustment | Store-and-forward
Phase 4 - Incentive Layer:
Token reward for fragment storage & relay | Proof-of-bandwidth consensus
Phase 5 - Application Layer:
MegaNet DNS equivalent | Browser extension | Mobile app

## Slide 13
The internet can be rebuilt.
No IPs. No DNS. No censorship.
Code: /usr/src/meganet | Run: python main.py
MegaNet MVP | Hacking Conference 2026 | Questions?